## Slide 1: Kriging with Iterative Spatial Prediction of Uncertainty KRISP-U
Matthew Burnett
Department of Mechanical Engineering
University of South Carolina

## Slide 2: Motivation
Reduce the number of data points needed to characterize experimental domains
  Specifically, in cases where sampling is expensive or otherwise arduous

## Slide 3: Algorithm
The algorithm uses LOO resampling to estimate uncertainty of the model spatially
It compares the full model, , to a model missing one-point, using KL-divergence
The divergence is then assigned to the point removed and the set of points is interpolated to predict the uncertainty of the entire field

## Slide 4: KRISP-U
fit():
  Fits the kriging model to the dataset and predicts over a grid.
evaluate():
  Evaluates the model using cross-validation and computes uncertainties.
interpolate_uncertainty()
  Interpolates uncertainties over a spatial grid.
print_stats()
  Prints statistics of the fitted model.
get_stats()
  Analyzes the variogram of the fitted model.

## Slide 5: Model Selection
Proper variogram selection is essential the model will be meaningless otherwise
  If enable_plotting is True the variogram will be plotted for you
  Scikit has a great tutorial on variogram selection
  Any variogram in the PyKrige library can be used
Universal or Ordinary Kriging can be selected
  The difference is Ordinary kriging assumes a constant mean while Universal Kriging assumes the mean drifts

## Slide 6: Fitting and Evaluation
The model both predicts the expected values and the error spatially, additionally it recommends the optimal testing location (where uncertainty is maximum)

## Slide 7: Simulated Iterative Sampling
Has tendency to resample locations
Effectively reduces total uncertainty in simulated cases